## Slide 1: Teleconference with noise and eco cancellation
EQ2440 Project in Wireless Communication
Group:
Animesh Das
Jonas Sedin
Mohammad Abdulla
Thomas Gaudy
Xavier Bush
Advisor:
Per Zetterberg

## Slide 2: Background
  The first recognized work and patent on eliminating noise from speech signal was documented in 1934.
  In 1950, a systems was designed where the noise in helicopter and airplane cockpits communication were canceled.
  In 1985, a highly efficient Short-Time Spectral Amplitude (STSA) estimator for speech signals to minimize the mean square error of the log-spectra was developed.

## Slide 3: Problem Formulation
The diversity of noise nature and its sources lead to a big challenge
  Develop high performance solutions in these diverse environments.
  Important to take into account the variability that the noise may experience.
  Different classification of the noise
    Duration of the noise sequences, color of the noise and stationarity
    Therefore, a lot of systems are using combined techniques to reach the best possible performance

## Slide 4: Approaches
Two approaches
  Noise cancellation
  Speech enhancement

## Slide 5: Noise cancellation

## Slide 6: Noise cancellation - LMS
LMS – Least Mean Square
Updated through
In this case is our noisy voice, and Y is our pure noise
We used a filter of 1000 samples
Simplicity of O(n)

## Slide 7: Speech enhancement
Single microphone approach
Transform and block-based
Instead of cancelling the noise, approximate the voice
Our method is based on the paper ”Speech Enhancement using a minimum mean square error log-spectral Amplitude Estimator”(Ephraim, 1985)

## Slide 8: LogMMSE
Overlapping frames and windowing
FFT
Processing functions to estimate the speech
IFFT
Overlap and add

## Slide 9: logMMSE
The Fourier series coefficients of the noise and voice can be modelled as statistically independent Gaussian random variables
Motivated by the Central Limit theorem
We want to minimize the function

## Slide 10: logMMSE
This can be shown to be
What we have to solve is
With
and

## Slide 11: logMMSE
In the end it is solved by
A priori SNR
A posteriori SNR
The two problems lies in estimating the variance of the voice and the noise

## Slide 12: logMMSE
The noise variance is calculated in pauses where there is no speech
The a priori SNR is calculated using a ”Decision-directed estimation”

## Slide 13: Unsuccessful approaches
RLS
- Computationally infeasible
Frequency LMS
- Not enough noise reduction
Kalman filter
- Difficult to postulate a state space model
- Also computationally infeasible
Lattice Recursive Least Squares
- Instable and difficult to implement

## Slide 14: Android
Setup

## Slide 15: Android
State Machine

## Slide 16: Android
App Interface

## Slide 17: Conclusions
  Theory results
  LMS provides a big reduction of the noise
  logMMSE after LMS removes almost the 100% of the noise
Android results
  Distance between phones affects correlation
  Correlation affects filter order (5m => order 163)
  Big order => voice distortion
  Trade-off between noise cancellation and voice distortion
  Static phones limitation
  Set-up for good results
    Distance between Sender Phone and Noise Phone: 0.5 m
    Order of NLMS: 10-50

## Slide 18: Future Work
Proposal for future projects
  Reach a non-static application
  Reach phonic isolation between the Sender Phone and the Noise phone
  Reach maximum correlation between the additive noise of the Sender Phone with the pure noise recording
  Echo cancellation: enable hands free

## Slide 19: Potential Application

## Slide 20: Thank you