## Slide 1: Teleconference with noise and eco cancellation
EQ2440 Project in Wireless Communication
Group:
Animesh Das
Jonas Sedin
Mohammad Abdulla
Thomas Gaudy
Xavier Bush
Advisor:
Per Zetterberg

## Slide 2: Motivation
Background
  The first recognized work and patent on eliminating noise from speech signal was documented in 1934. [1]
  In 1950, a systems was designed where the noise in helicopter and airplane cockpits communication were canceled. [2]
  In 1985, Y. Ephraim and D. Malah developed a highly efficient Short-Time Spectral Amplitude (STSA) estimator for speech signals to minimize the mean square error of the log-spectra. [3]
Motivation
Problem Formulation
System Model
Techniques Overview
Result
Conclusion
Future Work

## Slide 3: Motivation
Possible Solutions
  LMS
  Wiener Non-Casual Filtering
  logMMSE
  LMS combined with logMMSE
  RLS algorithm
  Kalman filter
Motivation
Problem Formulation
System Model
Techniques Overview
Result
Conclusion
Future Work

## Slide 4: Motivation
Successful approaches
  LMS, good but have greater residual noise compared to combined techniques
  Wiener Non-Casual Filtering, unstable behavior in non-casual filtering
  LogMMSE, best performance with outstanding results of noise cancellation
Motivation
Problem Formulation
System Model
Techniques Overview
Result
Conclusion
Future Work

## Slide 5: Motivation
Unsuccessful approaches
  RLS algorithm is computationally heavier, took long time to process thus dropped after checking the computational cost
  Kalman filter,, main drawbacks : computational cost is too high. Difficulties to find a right State-Space Model.
Motivation
Problem Formulation
System Model
Techniques Overview
Result
Conclusion
Future Work

## Slide 6: Problem Formulation
The diversity of noise nature and its sources lead the engineering to a big challenge
  Develop high performance solutions in these diverse environments.
  Important to take into account the variability that the noise may experience
  Different classification of the noise
    Duration of the noise sequences, color of the noise and stationarity
    Therefore, a lot of systems are using combined techniques to reach the best possible performance
Motivation
Problem Formulation
System Model
Techniques Overview
Result
Conclusion
Future Work

## Slide 7: Android

## Slide 8: Techniques Overview
….
  …
  …
….
  …
  …
  …
  …
Motivation
Problem Formulation
System Model
Techniques Overview
Result
Conclusion
Future Work

## Slide 9: Result
….
…
…
Motivation
Problem Formulation
System Model
Techniques Overview
Result
Conclusion
Future Work

## Slide 10: Result
…
Motivation
Problem Formulation
System Model
Techniques Overview
Result
Conclusion
Future Work

## Slide 11: Result
…
Scheme
  …
…
  …
Motivation
Problem Formulation
System Model
Techniques Overview
Result
Conclusion
Future Work

## Slide 12: Result
…
…
  ….
…
  …
  …
…
  …
  …
Motivation
Problem Formulation
System Model
Techniques Overview
Result
Conclusion
Future Work

## Slide 13: Conclusion
  The impact of the noise cancellation
  With LMS algoritm most of the noise was reduced
  With LMS and logMMSE almost all noise was reduced
…
  …
  …
  …
    ….
    …
Motivation
Problem Formulation
System Model
Techniques Overview
Result
Conclusion
Future Work

## Slide 14: Future Work
…
  …
  …
  …
…
Motivation
Problem Formulation
System Model
Techniques Overview
Result
Conclusion
Future Work

## Slide 15: Thank you.

## Slide 16: References
[1] https://www.google.com/patents/US2043416
[2] https://www.google.com/patents/US2866848
[3] Y. Ephraim and D. Malah, “Speech enhancement using a minimum mean-square error log-spectral amplitude estimator,” IEEE Trans. Acoustic Speech, Signal Processing, Vol. ASSP-33, pp 443-445, Apr. 1985.